## Slide 1: Module Objectives
Module Title: LAN Security Concepts
Module Objective: Explain how vulnerabilities compromise LAN security
Topic Title | Topic Objective
Endpoint Security | Explain how to use endpoint security to mitigate attacks
Access Control | Explain how AAA and 802.1x are used to authenticate LAN endpoints and devices
Layer 2 Security Threats | Identify Layer 2 vulnerabilities
MAC Address Table Attack | Explain how a MAC address table attack compromised LAN security
LAN Attacks | Explain how LAN attacks compromise LAN security
Notes: 1
10- Introduction
10.0.2 – What will I learn in this module

## Slide 2: What Will You Learn?
Endpoints are particularly susceptible to malware-related attacks that originate through email or web browsing, such as DDOS, date breaches, and malware. These endpoints have typically used traditional host-based security features, such as antivirus/antimalware, host-based firewalls, and host-based intrusion prevention systems (HIPSs). Endpoints are best protected by a combination of NAC, host-based AMP software, an email security appliance (ESA), and a web security appliance (WSA).
AAA controls who is permitted to access a network (authenticate), what they can do while they are there (authorize), and to audit what actions they performed while accessing the network (accounting).
The IEEE 802.1X standard is a port-based access control and authentication protocol that restricts unauthorized workstations from connecting to a LAN through publicly accessible switch ports.
If Layer 2 is compromised, then all layers above it are also affected. The first step in mitigating attacks on the Layer 2 infrastructure is to understand the underlying operation of Layer 2 and the Layer 2 solutions: Port Security, DHCP Snooping, DAI, and IPSG. These won’t work unless management protocols are secured.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module?

## Slide 3: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
MAC address flooding attacks bombard the switch with fake source MAC addresses until the switch MAC address table is full.
A VLAN hopping attack enables traffic from one VLAN to be seen by another VLAN without the aid of a router.
A VLAN double-tagging attack is unidirectional and works only when the threat actor is connected to a port residing in the same VLAN as the native VLAN of the trunk port.
VLAN hopping and VLAN double-tagging attacks can be prevented by implementing the following trunk security guidelines:
  Disable trunking on all access ports.
  Disable auto trunking on trunk links so that trunks must be manually enabled.
  Be sure that the native VLAN is only used for trunk links.
Two types of DHCP attacks are DHCP starvation and DHCP spoofing. Both attacks are mitigated by implementing DHCP snooping.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)

## Slide 4: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
ARP Attack: A threat actor sends a gratuitous ARP message containing a spoofed MAC address to a switch, and the switch updates its MAC table accordingly. Now the threat actor sends unsolicited ARP Replies to other hosts on the subnet with the MAC Address of the threat actor and the IP address of the default gateway. ARP spoofing and ARP poisoning are mitigated by implementing DAI.
Address Spoofing Attack: IP address spoofing is when a threat actor hijacks a valid IP address of another device on the subnet or uses a random IP address. MAC address spoofing attacks occur when the threat actors alter the MAC address of their host to match another known MAC address of a target host. IP and MAC address spoofing can be mitigated by implementing IPSG.
STP Attack: Threat actors manipulate STP to conduct an attack by spoofing the root bridge and changing the topology of a network. Threat actors make their hosts appear as root bridges; therefore, capturing all traffic for the immediate switched domain. This STP attack is mitigated by implementing BPDU Guard on all access ports.
CDP Reconnaissance: CDP information is sent out CDP-enabled ports in periodic, unencrypted broadcasts. CDP information includes the IP address of the device, IOS software version, platform, capabilities, and the native VLAN. The device receiving the CDP message updates its CDP database. the information provided by CDP can also be used by a threat actor to discover network infrastructure vulnerabilities. To mitigate the exploitation of CDP, limit the use of CDP on devices or ports.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)
10.6.2 – Module Quiz – LAN Security Concepts

## Slide 5: Module 10: LAN Security Concepts New Terms and Commands
Data Breach
Malware
Next-Generation Firewall (NGFW)
Next-Generation IPS (NGIPS)
Advanced Malware Protection (AMP)
Authentication, Authorization, Accounting (AAA)
Identity Services Engine (ISE)
Host-Based Intrusion Prevention System (HIPS)
Email Security Appliance (ESA)
Web Security Appliance (WSA)
login {local}
Remote Authentication Dial-In User Service (RADIUS)
Terminal Access Controller Access Control System (TACACS+)
IEEE 802.1X
Client (Supplicant)
Authenticator
Port Security
DHCP Snooping
Dynamic ARP Inspection (DAI)
IP Source Guard (IPSG)
VLAN Hopping
VLAN Double-Tagging
DHCP Starvation
DHCP Spoofing
Gratuitous ARP
ARP Spoofing
ARP Poisoning
Cisco Discovery Protocol (CDP)
no cdp run
no cdp enable
no lldp run
no lldp transmit | receive

## Slide 6: Module Objectives
Module Title: Switch Security Configuration
Module Objective: Configure switch security to mitigate LAN attacks
Topic Title | Topic Objective
Implement Port Security | Implement port security to mitigate MAC address table attacks.
Mitigate VLAN Attacks | Explain how to configure DTP and native VLAN to mitigate VLAN attacks.
Mitigate DHCP Attacks | Explain how to configure DHCP snooping to mitigate DHCP attacks.
Mitigate ARP Attacks | Explain how to configure ARP inspection to mitigate ARP attacks.
Mitigate STP Attacks | Explain how to configure PortFast and BPDU Guard to mitigate STP Attacks.
Proper CDP Usage | Best practices and avoiding CDP reconnaissance.
Notes: 6
11- Switch Security Configuration
11.0- Introduction
11.0.2 – What will I learn in this module?

## Slide 7: Module Practice and Quiz What Did I Learn In This Module?
All switch ports (interfaces) should be secured before the switch is deployed for production use.
By default, Layer 2 switch ports are set to dynamic auto (trunking on).
The simplest and most effective method to prevent MAC address table overflow attacks is to enable port security.
The switch can be configured to learn about MAC addresses on a secure port in one of three ways: manually configured, dynamically learned, and dynamically learned – sticky.
If the MAC address of a device attached to the port differs from the list of secure addresses, then a port violation occurs. By default, the port enters the error-disabled state. When a port is placed in the error-disabled state, no traffic is sent or received on that port.
Mitigate VLAN Hopping attacks by disabling DTP negotiations, disabling unused ports, manually setting trunking where required, and using a native VLAN other than VLAN 1.
Notes: 11 – Switch Security Configuration
11.6 – Module Practice and Quiz
11.6.3 – What Did I Learn In This Module?

## Slide 8: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
The goal of a DHCP starvation attack is to create a Denial of Service (DoS) for connecting clients. DHCP spoofing attacks can be mitigated by using DHCP snooping on trusted ports.
DHCP snooping determines whether DHCP messages are from an administratively-configured trusted or untrusted source. It then filters DHCP messages and rate-limits DHCP traffic from untrusted sources.
Dynamic ARP inspection (DAI) requires DHCP snooping and helps prevent ARP attacks by verifying ARP traffic.
Implement Dynamic ARP Inspection to mitigate ARP spoofing and ARP poisoning.
To mitigate Spanning Tree Protocol (STP) manipulation attacks, use PortFast and Bridge Protocol Data Unit (BPDU) Guard.
Notes: 11 – Switch Security Configuration
11.6 – Module Practice and Quiz
11.6.3 – What Did I Learn In This Module? (Cont.)
11.6.4 – Module Quiz

## Slide 9: Module 11: LAN Security Concepts New Terms and Commands
interface range
switchport port-security
switchport port-security interface
switchport port-security maximum
switchport port-security mac-address
switchport port-security mac-address sticky
switchport port-security aging time #
switchport port-security aging type
switchport port-security violation
show switchport port-security
switchport mode access|trunk
switchport nonegotiate
switchport trunk native vlan #
ip dhcp snooping
ip dhcp snooping vlan #
ip dhcp snooping limit rate
show ip dhcp snooping
ip arp inspection vlan #
ip dhcp snooping trust
ip arp inspection trust
ip arp inspection validate
spanning-tree portfast {default}
spanning-tree bpduguard enable
spanning-tree porfast bpduguard default