## Slide 1: LAN Security Concepts
Notes: Cisco Networking Academy Program
Switching, Routing and Wireless Essentials v7.0 (SRWE)
Module 10: LAN Security Concepts

## Slide 2: LAN Security Concepts
OSI reference model divided into seven layers which work independently of each other.
The figure shows the function of each layer and the core elements that can be exploited.
Network security solutions designed to protect the elements in Layer 3 up through Layer 7 include VPNs, firewalls, and IPS.
However, if Layer 2 is compromised, then all the layers above it are also affected.
For example, if a threat actor with access to the internal network captured Layer 2 frames, then all the security implemented on the layers above may be useless.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.1 - Layer 2 Vulnerabilities

## Slide 3: Layer 2 Security Threats Switch Attack Categories
Security is only as strong as the weakest link in the system, and Layer 2 is considered to be that weak link. Today with BYOD and more sophisticated attacks, our LANs have become more vulnerable to penetration.
Category | Examples
MAC Table Attacks | Includes MAC address flooding attacks.
VLAN Attacks | Includes VLAN hopping and VLAN double-tagging attacks. It also includes attacks between devices on a common VLAN.
DHCP Attacks | Includes DHCP starvation and DHCP spoofing attacks.
ARP Attacks | Includes ARP spoofing and ARP poisoning attacks.
STP Attacks | Includes Spanning Tree Protocol manipulation attacks.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.2 - Switch Attack Categories

## Slide 4: Layer 2 Security Threats Switch Attack Mitigation Techniques
Solution | Description
Port Security | Prevents many types of attacks including MAC address flooding attacks and DHCP starvation attacks.
DHCP Snooping | Prevents DHCP starvation and DHCP spoofing attacks.
Dynamic ARP Inspection (DAI) | Prevents ARP spoofing and ARP poisoning attacks.
IP Source Guard (IPSG) | Prevents MAC and IP address spoofing attacks.
These Layer 2 solutions will not be effective if the management protocols are not secured. The following strategies are recommended:
Always use secure variants of management protocols such as SSH, Secure Copy Protocol (SCP), Secure FTP (SFTP), and Secure Socket Layer/Transport Layer Security (SSL/TLS).
Consider using out-of-band management network to manage devices.
Use a dedicated management VLAN where nothing but management traffic resides.
Use ACLs to filter unwanted access.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.3 - Switch Attack Mitigation Techniques
10.3.4 – Check Your Understanding– Layer 2 Security Threats

## Slide 5: 10.4 MAC Address Table Attack
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack

## Slide 6: MAC Address Table Attack Switch Operation Review
Recall that to make forwarding decisions, a Layer 2 LAN switch builds a table based on the source MAC addresses in received frames. This is called a MAC address table. MAC address tables are stored in memory and are used to more efficiently switch frames.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.1 – Switch Operation Review

## Slide 7: MAC Address Table Attack MAC Address Table Flooding
All MAC tables have a fixed size and consequently, a switch can run out of resources in which to store MAC addresses. MAC address flooding attacks take advantage of this limitation by bombarding the switch with fake source MAC addresses until the switch MAC address table is full.
When this occurs, the switch treats the frame as an unknown unicast and begins to flood all incoming traffic out all ports on the same VLAN without referencing the MAC table. This condition now allows a threat actor to capture all of the frames sent from one host to another on the local LAN or local VLAN.
Note: Traffic is flooded only within the local LAN or VLAN. The threat actor can only capture traffic within the local LAN or VLAN to which the threat actor is connected.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.2 – MAC Address Table Flooding

## Slide 8: MAC Address Table Attack MAC Address Table Attack Mitigation
What makes tools such as macof so dangerous is that an attacker can create a MAC table overflow attack very quickly. For instance, a Catalyst 6500 switch can store 132,000 MAC addresses in its MAC address table. A tool such as macof can flood a switch with up to 8,000 bogus frames per second; creating a MAC address table overflow attack in a matter of a few seconds.
Another reason why these attack tools are dangerous is because they not only affect the local switch, they can also affect other connected Layer 2 switches. When the MAC address table of a switch is full, it starts flooding out all ports including those connected to other Layer 2 switches.
To mitigate MAC address table overflow attacks, network administrators must implement port security. Port security will only allow a specified number of source MAC addresses to be learned on the port. Port security is further discussed in another module.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.3 – MAC Address Table Attack Mitigation
10.4.4 – Check Your Understanding – MAC Address Table Attacks

## Slide 9: 10.5 LAN Attacks
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks

## Slide 10: LAN Attacks Video – VLAN and DHCP Attacks
This video will cover the following:
VLAN Hopping Attack
VLAN Double-Tagging Attack
DHCP Starvation Attack
DHCP Spoofing Attack
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.1 – Video – VLAN and DHCP Attacks

## Slide 11: LAN Attacks VLAN Hopping Attacks
A VLAN hopping attack enables traffic from one VLAN to be seen by another VLAN without the aid of a router. In a basic VLAN hopping attack, the threat actor configures a host to act like a switch to take advantage of the automatic trunking port feature enabled by default on most switch ports.
The threat actor configures the host to spoof 802.1Q signaling and Cisco-proprietary Dynamic Trunking Protocol (DTP) signaling to trunk with the connecting switch. If successful, the switch establishes a trunk link with the host, as shown in the figure. Now the threat actor can access all the VLANs on the switch. The threat actor can send and receive traffic on any VLAN, effectively hopping between VLANs.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.2 – VLAN Hopping Attacks

## Slide 12: LAN Attacks VLAN Double-Tagging Attacks
A threat actor is specific situations could embed a hidden 802.1Q tag inside the frame that already has an 802.1Q tag. This tag allows the frame to go to a VLAN that the original 802.1Q tag did not specify.
Step 1: The threat actor sends a double-tagged 802.1Q frame to the switch. The outer header has the VLAN tag of the threat actor, which is the same as the native VLAN of the trunk port.
Step 2: The frame arrives on the first switch, which looks at the first 4-byte 802.1Q tag. The switch sees that the frame is destined for the native VLAN. The switch forwards the packet out all native VLAN ports after stripping the VLAN tag. The frame is not retagged because it is part of the native VLAN. At this point, the inner VLAN tag is still intact and has not been inspected by the first switch.
Step 3: The frame arrives at the second switch which has no knowledge that it was supposed to be for the native VLAN. Native VLAN traffic is not tagged by the sending switch as specified in the 802.1Q specification. The second switch looks only at the inner 802.1Q tag that the threat actor inserted and sees that the frame is destined the target VLAN. The second switch sends the frame on to the target or floods it, depending on whether there is an existing MAC address table entry for the target.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.3 – VLAN Double-Tagging Attacks

## Slide 13: LAN Attacks VLAN Double-Tagging Attacks (Cont.)
A VLAN double-tagging attack is unidirectional and works only when the attacker is connected to a port residing in the same VLAN as the native VLAN of the trunk port. The idea is that double tagging allows the attacker to send data to hosts or servers on a VLAN that otherwise would be blocked by some type of access control configuration. Presumably the return traffic will also be permitted, thus giving the attacker the ability to communicate with devices on the normally blocked VLAN.
VLAN Attack Mitigation - VLAN hopping and VLAN double-tagging attacks can be prevented by implementing the following trunk security guidelines, as discussed in a previous module:
  Disable trunking on all access ports.
  Disable auto trunking on trunk links so that trunks must be manually enabled.
  Be sure that the native VLAN is only used for trunk links.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.3 – VLAN Double-Tagging Attacks (Cont.)

## Slide 14: LAN Attacks DHCP Messages
DHCP servers dynamically provide IP configuration information including IP address, subnet mask, default gateway, DNS servers, and more to clients. A review of the sequence of the DHCP message exchange between client and server is show in the figure.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.4 – DHCP Messages

## Slide 15: LAN Attacks DHCP Attacks
Two types of DHCP attacks are DHCP starvation and DHCP spoofing. Both attacks are mitigated by implementing DHCP snooping.
DHCP Starvation Attack – The goal of this attack is to create a DoS for connecting clients. DHCP starvation attacks require an attack tool such as Gobbler. Gobbler has the ability to look at the entire scope of leasable IP addresses and tries to lease them all. Specifically, it creates DHCP discovery messages with bogus MAC addresses.
DHCP Spoofing Attack – This occurs when a rogue DHCP server is connected to the network and provides false IP configuration parameters to legitimate clients. A rogue server can provide a variety of misleading information, including the following:
    Wrong default gateway - The rogue server provides an invalid gateway or the IP address of its host to create a man-in-the-middle attack. This may go entirely undetected as the intruder intercepts the data flow through the network.
    Wrong DNS server - The rogue server provides an incorrect DNS server address pointing the user to a nefarious website.
    Wrong IP address - The rogue server provides an invalid IP address effectively creating a DoS attack on the DHCP client.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.5 – DHCP Attacks

## Slide 16: LAN Attacks Video – ARP Attacks, STP Attacks, and CDP Reconnaissance
This video will cover the following:
ARP Spoofing Attack
ARP Poisoning Attack
STP Attack
CDP Reconnaissance
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.6 - Video – ARP Attacks, STP Attacks, and CDP Reconnaissance

## Slide 17: LAN Attacks ARP Attacks
Hosts broadcast ARP Requests to determine the MAC address of a host with a destination IP address. All hosts on the subnet receive and process the ARP Request. The host with the matching IP address in the ARP Request sends an ARP Reply.
A client can send an unsolicited ARP Reply called a “gratuitous ARP”. Other hosts on the subnet store the MAC address and IP address contained in the gratuitous ARP in their ARP tables.
An attacker can send a gratuitous ARP message containing a spoofed MAC address to a switch, and the switch would update its MAC table accordingly. In a typical attack, a threat actor sends unsolicited ARP Replies to other hosts on the subnet with the MAC Address of the threat actor and the IP address of the default gateway, effectively setting up a man-in-the-middle attack.
There are many tools available on the internet to create ARP man-in-the-middle attacks.
IPv6 uses ICMPv6 Neighbor Discovery Protocol for Layer 2 address resolution. IPv6 includes strategies to mitigate Neighbor Advertisement spoofing, similar to the way IPv6 prevents a spoofed ARP Reply.
ARP spoofing and ARP poisoning are mitigated by implementing Dynamic ARP Inspection (DAI).
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.7- ARP Attacks

## Slide 18: LAN Attacks Address Spoofing Attacks
IP address spoofing is when a threat actor hijacks a valid IP address of another device on the subnet or uses a random IP address. IP address spoofing is difficult to mitigate, especially when it is used inside a subnet in which the IP belongs.
MAC address spoofing attacks occur when the threat actors alter the MAC address of their host to match another known MAC address of a target host. The switch overwrites the current MAC table entry and assigns the MAC address to the new port. It then inadvertently forwards frames destined for the target host to the attacking host.
When the target host sends traffic, the switch will correct the error, realigning the MAC address to the original port. To stop the switch from returning the port assignment to its correct state, the threat actor can create a program or script that will constantly send frames to the switch so that the switch maintains the incorrect or spoofed information.
There is no security mechanism at Layer 2 that allows a switch to verify the source of MAC addresses, which is what makes it so vulnerable to spoofing.
IP and MAC address spoofing can be mitigated by implementing IP Source Guard (IPSG).
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.8 – Address Spoofing Attacks

## Slide 19: LAN Attacks STP Attack
Network attackers can manipulate the Spanning Tree Protocol (STP) to conduct an attack by spoofing the root bridge and changing the topology of a network. Attackers can then capture all traffic for the immediate switched domain.
To conduct an STP manipulation attack, the attacking host broadcasts STP bridge protocol data units (BPDUs) containing configuration and topology changes that will force spanning-tree recalculations. The BPDUs sent by the attacking host announce a lower bridge priority in an attempt to be elected as the root bridge.
This STP attack is mitigated by implementing BPDU Guard on all access ports. BPDU Guard is discussed in more detail later in the course.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.9 – STP Attack

## Slide 20: LAN Attacks CDP Reconnaissance
The Cisco Discovery Protocol (CDP) is a proprietary Layer 2 link discovery protocol. It is enabled on all Cisco devices by default. Network administrators also use CDP to help configure and troubleshoot network devices. CDP information is sent out CDP-enabled ports in periodic, unencrypted, unauthenticated broadcasts. CDP information includes the IP address of the device, IOS software version, platform, capabilities, and the native VLAN. The device receiving the CDP message updates its CDP database.
To mitigate the exploitation of CDP, limit the use of CDP on devices or ports. For example, disable CDP on edge ports that connect to untrusted devices.
  To disable CDP globally on a device, use the no cdp run global configuration mode command. To enable CDP globally, use the cdp run global configuration command.
  To disable CDP on a port, use the no cdp enable interface configuration command. To enable CDP on a port, use the cdp enable interface configuration command.
Note: Link Layer Discovery Protocol (LLDP) is also vulnerable to reconnaissance attacks. Configure no lldp run to disable LLDP globally. To disable LLDP on the interface, configure no lldp transmit and no lldp receive.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.10 – CDP Reconnaissance
10.5.11 – Check Your Understanding – LAN Attacks

## Slide 21: 10.6 Module Practice and Quiz
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz

## Slide 22: Module Practice and Quiz What Did I Learn In This Module?
Endpoints are particularly susceptible to malware-related attacks that originate through email or web browsing, such as DDOS, date breaches, and malware. These endpoints have typically used traditional host-based security features, such as antivirus/antimalware, host-based firewalls, and host-based intrusion prevention systems (HIPSs). Endpoints are best protected by a combination of NAC, host-based AMP software, an email security appliance (ESA), and a web security appliance (WSA).
AAA controls who is permitted to access a network (authenticate), what they can do while they are there (authorize), and to audit what actions they performed while accessing the network (accounting).
The IEEE 802.1X standard is a port-based access control and authentication protocol that restricts unauthorized workstations from connecting to a LAN through publicly accessible switch ports.
If Layer 2 is compromised, then all layers above it are also affected. The first step in mitigating attacks on the Layer 2 infrastructure is to understand the underlying operation of Layer 2 and the Layer 2 solutions: Port Security, DHCP Snooping, DAI, and IPSG. These won’t work unless management protocols are secured.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module?

## Slide 23: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
MAC address flooding attacks bombard the switch with fake source MAC addresses until the switch MAC address table is full.
A VLAN hopping attack enables traffic from one VLAN to be seen by another VLAN without the aid of a router.
A VLAN double-tagging attack is unidirectional and works only when the threat actor is connected to a port residing in the same VLAN as the native VLAN of the trunk port.
VLAN hopping and VLAN double-tagging attacks can be prevented by implementing the following trunk security guidelines:
  Disable trunking on all access ports.
  Disable auto trunking on trunk links so that trunks must be manually enabled.
  Be sure that the native VLAN is only used for trunk links.
Two types of DHCP attacks are DHCP starvation and DHCP spoofing. Both attacks are mitigated by implementing DHCP snooping.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)

## Slide 24: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
ARP Attack: A threat actor sends a gratuitous ARP message containing a spoofed MAC address to a switch, and the switch updates its MAC table accordingly. Now the threat actor sends unsolicited ARP Replies to other hosts on the subnet with the MAC Address of the threat actor and the IP address of the default gateway. ARP spoofing and ARP poisoning are mitigated by implementing DAI.
Address Spoofing Attack: IP address spoofing is when a threat actor hijacks a valid IP address of another device on the subnet or uses a random IP address. MAC address spoofing attacks occur when the threat actors alter the MAC address of their host to match another known MAC address of a target host. IP and MAC address spoofing can be mitigated by implementing IPSG.
STP Attack: Threat actors manipulate STP to conduct an attack by spoofing the root bridge and changing the topology of a network. Threat actors make their hosts appear as root bridges; therefore, capturing all traffic for the immediate switched domain. This STP attack is mitigated by implementing BPDU Guard on all access ports.
CDP Reconnaissance: CDP information is sent out CDP-enabled ports in periodic, unencrypted broadcasts. CDP information includes the IP address of the device, IOS software version, platform, capabilities, and the native VLAN. The device receiving the CDP message updates its CDP database. the information provided by CDP can also be used by a threat actor to discover network infrastructure vulnerabilities. To mitigate the exploitation of CDP, limit the use of CDP on devices or ports.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)
10.6.2 – Module Quiz – LAN Security Concepts

## Slide 25: Module 10: LAN Security Concepts New Terms and Commands
Data Breach
Malware
Next-Generation Firewall (NGFW)
Next-Generation IPS (NGIPS)
Advanced Malware Protection (AMP)
Authentication, Authorization, Accounting (AAA)
Identity Services Engine (ISE)
Host-Based Intrusion Prevention System (HIPS)
Email Security Appliance (ESA)
Web Security Appliance (WSA)
login {local}
Remote Authentication Dial-In User Service (RADIUS)
Terminal Access Controller Access Control System (TACACS+)
IEEE 802.1X
Client (Supplicant)
Authenticator
Port Security
DHCP Snooping
Dynamic ARP Inspection (DAI)
IP Source Guard (IPSG)
VLAN Hopping
VLAN Double-Tagging
DHCP Starvation
DHCP Spoofing
Gratuitous ARP
ARP Spoofing
ARP Poisoning
Cisco Discovery Protocol (CDP)
no cdp run
no cdp enable
no lldp run
no lldp transmit | receive